# 6502 Basic Outline
## Requirements
### Free Software
Under the MIT license.
### Compatibility
Should run either on a 6502 , a 65C02 or similar processors.
### Modular design
Modules should be added or removed independently. Communication with modules is through an X dispatch block e.g. jmp (dispatchTable,x), with one entry point for each module, this allows paging etc.
### Modern
Should have modern features - Procedures, Local variables, Structures and so on. Three types (int % string $ float #, default variable)
### Extensible
Should be extensible with system specific functionality.
## Modules
Code for all optional modules is built in, but can generated an error and have no actual code. All module functionality is accessed through one function, at a slight cost in speed, so that modules can be paged.
### Main
Main evaluation and execution functions, standard integer functions, normal dispatch tables, standard procedures, variables, locals, structures, basic syntax checking routines.
### Error
Error handling, which can be localised.
### System
External I/O type functionality, System specific functionality.
### FloatingPoint (optional)
Handles all floating point operations. Code for FP types is built in, but when activated can cause an error.
### String (optional)
String functions and manager, handles concrete and temporary strings, garbage collection and so on. The default string handling (Atom style) is built in by default however.
### Assembler (optional)
65(C)02 inline assembler similar to the BBC Micro.
### Tokeniser (optional)
Line tokenising / detokenising. Contains the text for the keywords, may not be needed for a run-time only system.
### Editor (optional)
Code connected with editing, task switching and so on.
## Implementation
All module handlers should use the name of their module, together with a constant which is the name of the module, followed by an underscore followed by the method
e.g. editor_deleteline
This should be automatically generated from the files in the module subdirectory, which looks for marks as follows.
EditorDeleteLine:	;; <deleteline>
These constants will of course be even. A table of them will be created called <module>handlers: so you will end up with
editor_deleteline = 0
..
editor:	jmp	(editorhandlers,x)
editorhandlers:
.word	EditorDeleteLine
for example.
Each module is in its own subdirectory, with a <module>.asm which contains all the module components.
## Tokens
### Token Grouping
Group/Token	Constant	Contents
ASCII ($00-$39)		Used in identifier $2D (-) is used for underscore , allows A-Z 0-9 . and _
Type ($3A-$3F)	TOK_[ISR]<ARR>	Represent integer,string,real and the appropriate arrays, mark end of identifier. % %( $ $( # #(
Constant ($40-$7F)		Constant 0-63. Each successive constant shifts this left 6 pixels (in practice, left 8 right 2) and replaces the lower 6 bits.
End of Line ($80)	TOK_EOL	Indicates end of line
Token shift ($81-3)	TOK_SHIFT1..3	Shifts to other token sets, must be followed by $86-$FF
FP Constant ($84)	TOK_FPC	Marks a floating point constant, which is of size TOK_FPC_SIZE bytes including the constant.
String ($85)	TOK_STR	Marks a string, the length of the string follows (0-255 chars), ASCII 32..127 only.
Binary Operators	TOK_BINARYST	Binary operators : and or xor + - * / mod >> << ^ >= <= = <> > < ! ?
Structures	TOK_STRUCTST	Keywords which affect the structure level.
Unary Operators	TOK_UNARYST	Unary operators (mostly functions), but there are duplicate unaries for ! ? and -. Also ( is a unary function.
Keywords/Tokens	TOK_TOKENS	Other keywords and tokens and syntactic markers, general.

Keywords as far as TOK_UNARYST have an associated table which either identify them as commands or binary functions,structure modifiers or identify their precedence level.
Anything after TOK_TOKENS is just an straightforward Command entry.
$83 is reserved for floating point functions like LN and so on, the token is passed as a parameter to the floating point handler, and are all unary functions.

## Stack
The stack is the usual design. 6 bytes in sign, and either a 2 byte address (string) 4 byte constant (integer) or 4 byte mantissa and 1 byte exponent (floating point).
The type byte is :
Bit 7 :	indicates a reference (1) or constant (0).
Bit 6 : indicates integer/floating point (0) or string address (1).
Bits 1..5 : unused, currently 0.
Bit 0 : indicates integer (0) / floating point (1)
Note that a reference means something that can accommodate a value, string, fp or int, so while the string may be a reference of itself, this doesn’t mean it is a “storage slot”